## Slide 1
COMPUTER NETWORKS LAB PROJECT
Interactive Network Error Detection & Correction Simulator
A Comprehensive Mathematical Simulation of Data Link Layer Error Control Mechanisms Integrated with Network Simulator 2 (NS-2) Physical Channel Discrete-Event Modeling
PROJECT TEAM MEMBERS
AMAN KUMAR YADAV
• Parity & CRC Modulo-2 Division • Web Engine & Architecture
PRATIK BHARADBHUNJE
• Hamming Code Syndrome Calculation • Forward Error Correction
DEVRISHI GADIA
• Internet Checksum 1's Complement • NS-2 Channel Integration

## Slide 2
● EXECUTIVE SUMMARY
Project Motivation & Architectural Objectives
Bridging theoretical Data Link Layer error control with realistic physical channel noise modeling
1. The Problem in Physical Transmission
Real-world network transmission challenges:
• Physical Noise & Attenuation: Thermal noise, cross-talk, and fading corrupt binary bits (0 -> 1 or 1 -> 0) across copper and wireless media.
• Silent Data Corruption: Without Data Link Layer error detection, corrupted packets compromise application layer payloads, files, and protocols.
• Limitations of Textbook Theory: Traditional static exercises fail to show how check bits interact with live channel noise, loss rates, and syndrome recovery.
2. Our Integrated Solution
Complete interactive simulation suite:
• 5 Core Algorithms: Full implementation of 1D Parity, 2D Parity Matrix, Hamming Code (n,k), Internet Checksum, and Cyclic Redundancy Check (CRC).
• Network Simulator 2 (NS-2): Real discrete-event simulation via WSL with Node 0 (Tx), Node 1 (Rx), 2 Mbps link, and ErrorModel packet loss.
• Bit-Level Error Injection: Interactive bit-flipping, single-bit random noise, and 3-bit burst error corruption simulations.
• Multi-Platform Availability: Runs as high-performance Desktop GUI (Tkinter), Local Web Server (Python 3.14), and Cloud Web Application.

## Slide 3
● SYSTEM ARCHITECTURE
End-to-End Network Transmission Pipeline
The 6 architectural stages modeling sender encoding, channel transmission, noise, and receiver recovery
STAGE 01
Input Binary
Validation of binary stream (4, 8, 12, 16-bit presets or ASCII text converter).
STAGE 02
Encode & Redundancy
Generation of check bits, syndrome matrices, and transmitted codeword.
STAGE 03
Channel & NS-2
Physical transmission across duplex link with optional NS-2 ErrorModel loss.
STAGE 04
Error Injection
Interactive single-bit flip, random channel noise, or 3-bit burst corruption.
STAGE 05
Receiver Verify
Syndrome evaluation, 1's complement check, or Modulo-2 XOR division.
STAGE 06
Recovery & Result
Automated bit correction, diagnostic breakdown, and step-by-step visualizer.

## Slide 4
● ALGORITHM 1 OF 5
1D Parity Check (Even & Odd Schemes)
Minimal bandwidth redundancy mechanism for single-bit error detection
Mathematical Formulation & Working
Parity Bit Generation:
• Concept: Appends a single check bit (P) to the data stream such that the total count of binary 1s satisfies the chosen parity rule.
• Even Parity: P = 0 if sum of data bits is even; P = 1 if sum of data bits is odd. Formula: P = b1 ⊕ b2 ⊕ ... ⊕ bn
• Odd Parity: P = 1 if sum of data bits is even; P = 0 if sum of data bits is odd.
• Receiver Decision: Computes parity over received frame. If parity matches scheme -> Accepted; else -> Discarded (Error Detected).
• Detection Strength: Detects all odd numbers of bit errors (1, 3, 5...). Cannot detect even numbers of bit flips (2, 4...) because they cancel out parity.
NS-2 Physical Channel Simulation
Transmission across NS-2 Duplex Link:
• Codeword Transmission: Transmitter (Node 0) formats the frame (e.g. 11010010 + '0' = 110100100) and packetizes it into CBR UDP packets.
• NS-2 ErrorModel Loss: The duplex link applies a uniform loss probability. When an ErrorModel drop event occurs, a bit corruption event is registered.
• NS-2 Trace Output (.tr): Generated events record packet enqueue (+), drop (d), and receive (r) at Node 1 (Sink).
• Live Result: When NS-2 flips a single bit, the receiver parity check fails instantly, triggering 'Error Detected' with 100% reliability for 1-bit noise.

## Slide 5
● ALGORITHM 2 OF 5
2D Parity Check (Matrix Grid Localization)
Combining Longitudinal (LRC) & Vertical (VRC) Redundancy Checks for bit error correction
Matrix Organization & Error Pinpointing
Grid Coordinates and Parity Intersection:
• Matrix Structuring: Data stream of length M × N is organized into an M-row by N-column rectangular matrix grid.
• Row Parity (LRC): Computes horizontal parity for each row i (adds 1 bit per row).
• Column Parity (VRC): Computes vertical parity for each column j (adds 1 bit per column).
• Corner Parity: Calculates overall matrix parity bit at the bottom-right intersection.
• Intersection Localization: If bit at Row i, Column j is flipped, Row i parity FAILS and Column j parity FAILS. Their intersection (i, j) uniquely pinpoints the corrupted bit!
• Forward Error Correction: The receiver automatically inverts bit (i, j) back to its original state, achieving complete 1-bit recovery!
NS-2 Simulation & Recovery Demonstration
Channel Noise Modeling:
• Packet Serialization: The entire (M+1) × (N+1) codeword matrix is serialized and sent across NS-2 link from Node 0 to Node 1.
• NS-2 Trace Validation: Trace log ns2_parity2d.tr confirms packet transmission across the link with ErrorModel packet drops.
• Observed Behavior: When NS-2 corrupts a packet in transit, the receiver reconstructs the grid, detects the failed row and column, and corrects the bit seamlessly.
• Limitation Handled: If multiple bits flip across different rows/columns, the system flags 'Multiple Errors Detected (Uncorrectable)' accurately.

## Slide 6
● ALGORITHM 3 OF 5
Hamming Code (n, k) & Forward Error Correction
Power-of-two parity placement with mathematical syndrome calculation for automatic bit recovery
Mathematical Foundation & Syndrome Theory
Richard Hamming (1950) Coding Theory:
• Check Bit Placement: For k data bits, r parity bits are inserted at power-of-two bit indices (1, 2, 4, 8, ...) where 2^r >= k + r + 1.
• Bit Coverage: Parity bit at position 2^i checks all bit positions whose binary index has a 1 in the i-th bit position: • P1 checks [1, 3, 5, 7, 9, 11...] • P2 checks [2, 3, 6, 7, 10, 11...] • P4 checks [4, 5, 6, 7, 12, 13...]
• Syndrome Calculation: Receiver recalculates parity checks: Syndrome S = (s_r ... s_2 s_1)_2. • S = 0 => No error (Frame is clean) • S = Decimal value D => EXACT bit at position D is corrupted!
• Automatic Bit Flipping: Codeword[D] = ~Codeword[D]. The corrupted bit is inverted and original data is extracted with 100% accuracy.
NS-2 Simulation & Syndrome Execution
Discrete-Event Link Validation:
• NS-2 Trace Engine: Hamming codeword (e.g. 7-bit codeword for 4-bit data) transmitted across Node 0 -> Node 1 link.
• Trace Events in ns2_hamming.tr: Logs packets undergoing transmission (+) and ErrorModel drops (d).
• Syndrome Localization Demo: When NS-2 injects channel corruption, the simulator calculates the exact syndrome index (e.g. Syndrome = 5), highlights position 5 in yellow, and flips it back to original value.
• Industrial Relevance: Core algorithm used in ECC RAM (Server Memory), RAID-2 disk arrays, and satellite communication links.

## Slide 7
● ALGORITHM 4 OF 5
Internet Checksum (1's Complement Summation)
The foundational error detection mechanism powering IPv4, TCP, and UDP packet headers
Mathematical Mechanism & 1's Complement
RFC 1071 Standard Protocol Mechanism:
• Block Segmentation: The binary message stream is divided into k-bit blocks (typically 4, 8, or 16 bits).
• 1's Complement Addition: Sender adds all k-bit words together using standard binary addition.
• End-Around Carry: Whenever an overflow carry bit exceeds k bits, it is wrapped around and added to the least significant bit (LSB).
• Checksum Inversion: The final running sum is inverted (1's complement: 0 -> 1, 1 -> 0) and appended to the payload.
• Receiver Verification: Receiver sums all message blocks PLUS the checksum. If all bits in the sum equal 1 (i.e. complemented result is 0), the packet is VALID; otherwise CORRUPTED!
NS-2 Channel Integration & Protocol Context
Evaluating Link Transmission:
• NS-2 Trace Modeling: The Checksum-protected frame is transmitted across the NS-2 channel from Node 0 to Node 1.
• Trace Events in ns2_checksum.tr: Demonstrates packet drops and transmissions over 2 Mbps channel with 10 ms delay.
• Why Internet Protocols Use It: 1's complement summation is extremely fast to compute in software with simple integer additions, requiring minimal CPU cycles in routers.
• Observed Detection: Detects any burst error that alters the arithmetic sum. Clean frames yield complemented sum = 0x0000; corrupted frames yield non-zero sum.

## Slide 8
● ALGORITHM 5 OF 5
Cyclic Redundancy Check (CRC Modulo-2 Division)
High-performance polynomial division over GF(2) utilized in Ethernet, Wi-Fi, and USB
Polynomial Division over GF(2)
Binary Modulo-2 XOR Mathematics:
• Polynomial Representation: Binary data treated as coefficients of a polynomial M(x). Generator polynomial G(x) of degree r defines divisor.
• Sender Encoding: 1. Multiply M(x) by 2^r (append r zero bits to data). 2. Divide by G(x) using Modulo-2 division (XOR subtraction without borrow). 3. Remainder R(x) of r bits is the CRC Checksum. 4. Transmitted Codeword = M(x)*2^r + R(x).
• Receiver Verification: Receiver divides received frame by G(x). If Remainder == 0 => Clean (Accepted); If Remainder != 0 => Corrupted!
• Preset Polynomials Supported: • CRC-4 (ITU): 10011 (x^4 + x + 1) • CRC-8 (ATM): 100000111 • CRC-16 (IBM): 11000000000000101 • CRC-32 (IEEE 802.3 Ethernet): 33-bit polynomial
Detection Superiority & NS-2 Trace Integration
Industry-Standard Error Detection Power:
• 100% Single-Bit Errors: Any single-bit error is not divisible by G(x) (provided G(x) has at least 2 non-zero terms).
• 100% Double-Bit Errors: Detects all double-bit errors provided G(x) does not divide (x^k + 1).
• 100% Odd-Numbered Errors: If G(x) contains factor (x + 1), it catches ALL odd numbers of flipped bits.
• Burst Errors <= r Bits: Detects 100% of all burst error corruptions of length <= degree of G(x).
• NS-2 Integration (ns2_crc.tr): Transmits CRC codeword over NS-2 link. Channel packet drops trigger non-zero syndrome remainder at receiver sink.

## Slide 9
● CHANNEL SIMULATION ENGINE
Network Simulator 2 (NS-2) Integration Architecture
Coupling physical link discrete-event simulation with Data Link Layer error control
OTcl Network Topology Configuration
Physical Channel Modeling in network_error_sim.tcl:
• Simulator Engine: NS-2 discrete-event network simulator executed natively in WSL (/usr/bin/ns).
• Transmitter Node (n0): Agent/UDP attached to Node 0 with Constant Bit Rate (CBR) traffic generator sending 64-byte packets.
• Receiver Node (n1): Agent/Null sink attached to Node 1 acting as the destination receiver.
• Duplex Link: Bandwidth: 2.0 Mbps, Propagation Delay: 10 ms, Queueing: DropTail.
• ErrorModel Loss Module: Inserted directly on link n0 -> n1 with uniform random loss variable ($loss_module set rate_ $err_rate). Dropped packets routed to Agent/Null drop-target.
Trace Parsing & Python-to-NS-2 Bridge
Real-Time Trace File Analytics (.tr):
• Subprocess Bridge (ns2_bridge.py): Automates execution via 'wsl bash -c ns network_error_sim.tcl [params]', streaming stdout and return codes.
• Trace Event Parser: Parses 12-column NS-2 event records: • '+' : Packet queued at Transmitter (Node 0) • '-' : Packet transmitted onto physical link • 'd' : Packet DROPPED / CORRUPTED by ErrorModel • 'r' : Packet successfully received at Node 1 (Sink)
• Packet Error Rate (PER): Calculates PER = (Dropped / (Received + Dropped)) * 100%.
• NAM Visualizer Support: Generates network animation (.nam) files for visual packet flow inspection.

## Slide 10
● EMPIRICAL VALIDATION
Multi-Technique NS-2 Verification Matrix
Empirical benchmark proving that all 5 error detection techniques are 100% verified across NS-2
Technique | Transmitted Codeword | NS-2 Channel Link | ErrorModel PER | Receiver Status | NS-2 Status
1D Parity Check | 110100100 | Node 0 ➔ Node 1 (2 Mbps) | 20.0% ErrorModel | ✓ Parity Bit Verified | ✅ VERIFIED IN NS-2
2D Parity Matrix | 11011101001111... | Node 0 ➔ Node 1 (2 Mbps) | 20.0% ErrorModel | ✓ Row/Col Corrected | ✅ VERIFIED IN NS-2
Hamming Code (n,k) | 0110011 (7, 4) | Node 0 ➔ Node 1 (2 Mbps) | 20.0% ErrorModel | ✓ Syndrome Auto-Flip | ✅ VERIFIED IN NS-2
Internet Checksum | 1010100100111001... | Node 0 ➔ Node 1 (2 Mbps) | 20.0% ErrorModel | ✓ 1's Complement Inverted | ✅ VERIFIED IN NS-2
CRC Modulo-2 | 11010110111110 | Node 0 ➔ Node 1 (2 Mbps) | 20.0% ErrorModel | ✓ Remainder == 0 Checked | ✅ VERIFIED IN NS-2
Live Benchmark Execution via REST API (/api/run-ns2-all)
Our platform features a dedicated multi-technique batch runner that encodes data across all 5 algorithms, transmits each through NS-2 in WSL, logs separate trace files (ns2_parity.tr, ns2_parity2d.tr, ns2_hamming.tr, ns2_checksum.tr, ns2_crc.tr), and verifies error detection and bit correction live!

## Slide 11
● ALGORITHM COMPARISON
Comparative Analysis of All 5 Techniques
Comparing redundancy overhead, detection strength, correction capability, and protocol usage
Technique | Redundancy Overhead | Error Detection Power | Error Correction | Computational Cost | Standard Protocols
1D Parity | 1 bit | Single-bit & odd errors | None (Detection only) | O(n) - Single XOR | Async Serial (UART), ASCII
2D Parity Matrix | M + N + 1 bits | Burst errors & multiple bits | 1-bit error correction | O(M × N) Grid | Magnetic Tape, Telecommunications
Hamming Code | r bits (2^r >= m+r+1) | Single & double-bit errors | 1-bit forward correction | O(m log m) Syndrome | ECC RAM, RAID-2, Space Telemetry
Internet Checksum | 16 bits (typical) | Burst errors & sums | None (Detection only) | O(n) Integer addition | IPv4, TCP, UDP, ICMP
CRC Modulo-2 | Degree r of G(x) | 100% single/double/burst <= r | None (Detection only) | O(n) Bitwise shift/XOR | Ethernet, Wi-Fi 802.11, USB, SATA

## Slide 12
● SUMMARY & CONCLUSION
Implementation Highlights & Project Conclusion
Fully functional multi-platform simulator ready for live classroom and lab demonstrations
1. Key Implementation Accomplishments
Engineering Deliverables:
• Multi-Platform Architecture: Available as Tkinter desktop GUI (main.py) and modern responsive web application (localhost:5000 & Vercel cloud).
• Genuine NS-2 Integration: Automated OTcl script execution in WSL, live PER calculation, and 12-column event trace parsing.
• Interactive Learning Experience: Real-time bit clicking to inject channel noise, animated glowing ring feedback, and step-by-step mathematical visualizers.
• Zero Pip Dependencies for Core GUI: Desktop simulator runs cleanly using Python Standard Library alone.
2. Project Team & Demonstration Access
Developed by:
AMAN KUMAR YADAV PRATIK BHARADBHUNJE DEVRISHI GADIA
Computer Networks Lab Project
• Web Simulator URL: http://localhost:5000
• Local Wi-Fi Network Access: http://10.240.51.97:5000
• Source Code Repository: https://github.com/Amanyadav201205/errordetection
• Desktop Application: Run 'python main.py' or double-click 'run_app.bat'